## Slide 1: San Francisco Congestion Management Program
2019 Update
Citizens Advisory Committee Agenda Item 11
November 20, 2019

## Slide 2: CMP Purpose and Requirements
Purpose
    Define and report performance measures for congestion management
    Describe congestion management strategies and efforts; 2019-21 work program
Requirements
    Designated CMA updates every two years
    Auto Level-of-Service (LOS) and multimodal performance measures
    Travel Demand Management (TDM) and Land us impact analysis
    Capital Improvement Program (CIP)
Approval of CMP
Maintains city’s eligibility for state gas tax and other revenues
CMP Monitoring Network 2019
Notes: - As CMA, the Transportation Authority monitors and reports various performance measures on CMP network every two years.
CMP network includes over 230 miles of major arterials and freeways.
Requirements include monitoring Level-of-Service which is a measure of vehicle delay derived from auto speeds. However, we are unique in a way that we also measure several transit performance metrics in addition to automobile LOS.

## Slide 3: Automobile LOS Monitoring - 2019
    Level of Service (LOS): Measure of auto congestion, required standard by law.
    Average auto speeds decline further on CMP network
facility | period | 2017 | 2019 | Percent Change
Freeway | AM | 31.8 mph | 31.5 mph | -1%
Freeway | PM | 24.4 mph | 23.6 mph | -3%
Arterial | AM | 14 mph | 13.3 mph | -5%
Arterial | PM | 12.8 mph | 12.2 mph | -5%
Notes: As San Francisco continues to experience significant growth in jobs and population, auto speed decline further.
1-5% drop observed in auto speeds compared to last monitoring cycle.

## Slide 4: Performance Metric Trends
Chart: 
| 2011 | 2013 | 2015 | 2017
Arterial AM | 17.5582 | 17.1217 | 14.5985 | 13.5525
Arterial PM | 16.6349 | 15.9759 | 12.7394 | 12.1833
Freeway AM | 43.8587 | 39.2069 | 38.7535 | 35.7979
Freeway PM | 31.1615 | 29.3477 | 26.1931 | 26.3538
Arterial AM | 14 | 13.3
Arterial PM | 12.8 | 12.2
Freeway AM | 31.8 | 31.5
Freeway PM | 24.4 | 23.6
Auto Speeds
2019
DISCONNECT DUE TO DATA PRODUCT CHANGE FROM VENDOR
Transit (Bus) Speeds
Chart: 
| 2011 | 2013 | 2015 | 2017 | 2019
Transit Speed AM | 8.537 | 8.2534 | 8.2644 | 8.129 | 8.4425
Transit Speed PM | 7.8161 | 7.5489 | 7.3995 | 7.338 | 7.6043
2019

## Slide 5: Performance Metric Trends
Transit Reliability / Variability
Chart: 
| 2011 | 2013 | 2015 | 2017 | 2019
Variability AM | 0.29251 | 0.16026 | 0.15879 | 0.15886 | 0.21325
Variability PM | 0.30807 | 0.15985 | 0.1812 | 0.17889 | 0.20868
Chart: 
| 2011 | 2013 | 2015 | 2017 | 2019
Ratio AM | 2.0567 | 2.0745 | 1.7664 | 1.6672 | 1.5793
Ratio PM | 2.1283 | 2.1163 | 1.7217 | 1.6603 | 1.6047
Auto-Transit Speed Ratio

## Slide 6: Key Updates in 2019 CMP
    2019 system performance monitoring
      Automobile Level-of-Service (LOS or delay) monitoring
      Surface transit speed analysis
    Updates on TDM studies and initiatives
    Regional and State policy developments
    Travel forecasting improvements
    Capital Improvement Program (CIP): fund programming activities and project delivery progress
    Interactive visualization website updates
Notes: This CMP update also includes updates to TDM strategies, analysis of land use impacts on transportation, and the CIP chapter.
Interactive visualization updates. This significantly improves access to this data, and provides a means for the public to explore changes in transportation system performance over time
------------
-Consistent with SFTP
-TDM – SFTP recommendations, updates on Parking Pricing study, SFpark program, TI updates
-Land Use – reflects Plan Bay Area, Transportation Investment and Growth Strategy (TIGS), local efforts to link LU-T
-CIP consistent with latest TFCA programs, Lifeline Transportation Program, One Bay Area Grant, Prop AA Strategic Plan

## Slide 7: Congestion Data Visualization Website http://congestion.sfcta.org/

## Slide 8: Collision Data Visualization Website under development

## Slide 9: Thank you
Questions?

## Slide 10: INRIX Data Changes
Segment geographies modified
Data provider mix updated
Data to be more accurate and reliable
Results in a disconnect in trend lines
AVERAGE AUTO SPEED (MPH)
Chart: 
| 2011 | 2013 | 2015 | 2017
Arterial AM | 17.5582 | 17.1217 | 14.5985 | 13.5525
Arterial PM | 16.6349 | 15.9759 | 12.7394 | 12.1833
Freeway AM | 43.8587 | 39.2069 | 38.7535 | 35.7979
Freeway PM | 31.1615 | 29.3477 | 26.1931 | 26.3538
Arterial AM | 14 | 13.3
Arterial PM | 12.8 | 12.2
Freeway AM | 31.8 | 31.5
Freeway PM | 24.4 | 23.6
2019
DISCONNECT DUE TO DATA PRODUCT CHANGE FROM VENDOR

## Slide 11: Transit (Muni Bus) Speeds
Chart: 
| 2011 | 2013 | 2015 | 2017 | 2019
Transit Speed AM | 8.537 | 8.2534 | 8.2644 | 8.129 | 8.4425
Transit Speed PM | 7.8161 | 7.5489 | 7.3995 | 7.338 | 7.6043
AVERAGE SPEED (MPH)
 |  | 2017 | 2019 | % Change
Arterial | AM | 8.13 | 8.44 | 4%
Arterial | PM | 7.34 | 7.60 | 4%

## Slide 12: Transit (Muni Bus) Variability
Chart: 
| 2011 | 2013 | 2015 | 2017 | 2019
Variability AM | 0.29251 | 0.16026 | 0.15879 | 0.15886 | 0.21325
Variability PM | 0.30807 | 0.15985 | 0.1812 | 0.17889 | 0.20868
COEFFICIENT OF VARIATION
 |  | 2017 | 2019
Arterial | AM | 16% | 21%
Arterial | PM | 18% | 21%

## Slide 13: Auto-Transit (Bus) Speed Ratio
Chart: 
| 2011 | 2013 | 2015 | 2017 | 2019
Ratio AM | 2.0567 | 2.0745 | 1.7664 | 1.6672 | 1.5793
Ratio PM | 2.1283 | 2.1163 | 1.7217 | 1.6603 | 1.6047
 |  | 2017 | 2019 | % Change
Arterial | AM | 1.67 | 1.58 | -5%
Arterial | PM | 1.66 | 1.60 | -3%
AUTO-TRANSIT SPEED RATIO
 |  | 2017 | 2019
Arterial | AM | 1.67 | 1.58
Arterial | PM | 1.66 | 1.60

## Slide 14: ADT and Multimodal Count Locations

## Slide 15: Vehicle Counts
Chart: 
| AM | PM
2015 | 99485.0833 | 103803.5
2017 | 95914 | 100662.5
2019 | 93524.6333 | 97165.7667
ADT COUNTS (37 LOCATIONS)
INTERSECTION COUNTS (14 LOCATIONS)
Chart: 
| AM | PM
2015 | 74253 | 80141
2017 | 72722 | 78417
2019 | 70415 | 75009
᾽17
᾽18
᾽19
᾽17
᾽18
᾽19
᾽17
᾽18
᾽19
᾽17
᾽18
᾽19

## Slide 16: Bike-Ped Counts (14 Intersections)
Chart: BIKES
| AM | PM
2015 | 833 | 1428
2017 | 786 | 1334
2019 | 686 | 1409
Chart: PEDESTRIANS
| AM | PM
2015 | 21857 | 28563
2017 | 21204 | 29617
2019 | 20830 | 28264
᾽15
᾽17
᾽19
᾽15
᾽17
᾽19
᾽15
᾽17
᾽19
᾽15
᾽17
᾽19

## Slide 17: Collisions
INJURIES
FATALITIES
Chart: 
| 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016* | 2017* | 2018*
Pedestrian | 815 | 727 | 747 | 726 | 796 | 799 | 695 | 784 | 844 | 942 | 518 | 843 | 731 | 850 | 854 | 828
Bicycle | 311 | 316 | 343 | 343 | 451 | 468 | 531 | 599 | 630 | 658 | 454 | 657 | 574 | 566 | 562 | 583
Chart: 
| 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016* | 2017* | 2018*
Pedestrian | 25 | 20 | 14 | 15 | 24 | 13 | 17 | 14 | 17 | 16 | 21 | 18 | 25 | 19 | 15 | 15
Bicycle | 1 | 1 | 2 | 2 | 1 | 3 | 1 | 1 | 4 | 2 | 4 | 2 | 4 | 4 | 2 | 4
*Provisional SWITRS data (not final)

## Slide 18: VMT
Chart: DAILY VEHICLE MILES TRAVELED IN SAN FRANCISCO
| 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018
VMT | 9580.51 | 9993.26 | 9938.43 | 9856.2 | 9096.87 | 9442.7 | 9502.53 | 9293.8 | 8800.37 | 8796.87 | 8373.4 | 9009.77 | 8991.06 | 8812.17 | 8843.86 | 9580.01 | 9648.73

## Slide 19: Transit Ridership
Chart: AVERAGE DAILY RIDERSHIP BETWEEN 2010 AND 2019
| 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019
Muni | 676800 | 669800 | 701300 | 703300 | 705700 | 711000 | 726100 | 715700 | 711000 | 708300
BART | 334983.9315 | 345256.068 | 366564.804 | 392292.8502 | 399145 | 423119.8699 | 433394.0964 | 423395.4879 | 414166 | 410774
Caltrain | 34120 | 37779 | 42354 | 47060 | 52611 | 58245 | 62416 | 64114 | 65095 | 63597